## Slide 1: LC3 Final Project
Khalil Gammoh and Ammon Gruwell

## Slide 2: Overview
Test Plan
Test Strategy
Test Bench Block Diagram
Cover groups
Assertions
Tests applied
Bug Report

## Slide 3: Test Plan
All opcodes are supported
Instructions can be executed in any order
Instructions can be repeated
A load after a store returns the value previously written
A store command modifies memory correctly
Branching can jump forward or backward
Branching depends on n, z, and p
Any register can be a source
Any register can be a destination
Reset can happen during any clock cycle of LD
Reset can happen during any instruction

## Slide 4: Test Strategy
Cover Groups
  All opcodes used
  All opcodes are preceded and followed by all others
  All opcodes are followed by the same opcode
  Reset is tested during all cycles of Load
  Reset is tested with all opcodes
  Branch occurs with N, Z, and P
  All opcodes are tested with all SRC1, SRC2, and DST registers
Assertions
  Flags aren’t high at the same time
  Bus isn’t driven by more that one thing
  Registers are 0 after a reset
  MemWe is only ever high for one clock cycle
  Only store instructions write to memory
Tests
  Coverage
  Large number of instructions
  Different tests for different DUTs

## Slide 5: Test Approach Tradeoffs
Memory Model
  DUT memory module and golden memory array
  Memory locations are randomized at startup
  Instructions written to the DUT memory at Fetch
Checking Memory after each instruction
  Checking the entire memory took a long time so we only did it when necessary
  We check the current memory location only after each instruction
Handling two different DUTs
  We created different tests for each DUT which contains a Config flag
  Each time a cross module reference is needed we check the Config flag
DUT
TB
Golden Memory
Memory
Monitor
RST

## Slide 6: Test Bench Block Diagram
c
Test
Generator
Driver
Assertions
Scoreboard
Monitor
DUT
Functional Coverage
Environment

## Slide 7: Program Flow Diagram
Generator
Driver/ Golden Model
Trans
DUT
Instr
Monitor
ScoreBoard
State
State

## Slide 8: Bug Report
Date | Time | Minutes to Find/Fix | DUT Owner | Description
12/12/16 | 5:15 PM | 20 | Ammon | Memory out signal was being driven to bus instead of to the MDR
12/14/16 | 10:48 AM | 30 | Ammon | Trap was using the sign extended IR[8:0] instead of the zero extended IR[7:0] and was thus only taking one clock cycle
12/14/16 | 10:58 AM | 2 | Ammon | I was sign extending the trap vector instead of zero extending it.
12/14/16 | 5:54 PM | 2 | Khalil | We added a start state before fetch0 after reset
12/14/16 | 10:48 PM | 2 | Ammon | Reset was not included in memory module
12/15/16 | 1:10 AM | 60 | Khalil | Our enum type was too big so that when it was casted to an int it was getting chopped off
12/15/16 | 1:28 AM | 15 | Khalil | Our JSRR instruction was always using register 0 as its source register
12/15/16 | 2:02 AM | 15 | Khalil | DUT didn’t have reserved or RTI states in it
12/15/16 | 11:00 | 5 | Khalil | DUT was using synchronous resets for the registers

## Slide 9: Waveforms
Khalil’s LC3 (showing a reset)
Ammon’s LC3 (showing a reset)

## Slide 10: Functional Coverage

## Slide 11: Test Output
# // Questa Sim-64
# // Version 10.1c linux_x86_64 Jul 27 2012
# //
# // Copyright 1991-2012 Mentor Graphics Corporation
# // All Rights Reserved.
# //
# // THIS WORK CONTAINS TRADE SECRET AND PROPRIETARY INFORMATION
# // WHICH IS THE PROPERTY OF MENTOR GRAPHICS CORPORATION OR ITS
# // LICENSORS AND IS SUBJECT TO LICENSE TERMS.
# //
# vsim +TESTNAME=TestAmmonCov -do lc3.do opt
# Loading sv_std.std
# Loading work.lc3_top(fast)
# Loading work.test_if(fast)
# Loading work.lc3_pkg(fast)
# Loading work.lc3_tb(fast)
# Loading work.memory(fast)
# Loading work.ammon_lc3_sv_unit(fast)
# Loading work.ammon_lc3(fast)
# Loading work.ammon_lc3_datapath(fast)
# Loading work.register_t(fast)
# Loading work.tristate_driver(fast)
# Loading work.lc32dkhalil2dsv_sv_unit(fast)
# Loading work.MAR(fast)
# Loading work.MDR(fast)
# Loading work.khalil_LC3(fast)
# Loading work.Datapath(fast)
# Loading work.register(fast)
# Loading work.register_1bit(fast)
# Loading work.ControlUnit(fast)
# do lc3.do
# Registering class: TestAmmonCov
# Registering class: TestKhalilCov
# Registering class: TestAmmon
# Registering class: TestKhalil
# lc3_pkg.Factory.get_test found TESTNAME=TestAmmonCov
# lc3_pkg.TestAmmonCov.new
# Built Environment in TestBasic
# 3.6525e+08 Test Coverage reached 100 percent! Exiting test after 68964 instructions...
# ** Note: $finish : lc3_pkg.sv(225)
# Time: 36524950 ns Iteration: 3 Region: /lc3_pkg::Environment::run